## Slide 1: How to Solder
Captain Matt Audette
Jan 2017
mraudett@nps.edu
404-304-9903

## Slide 2: Topics Covered
Overview
Minimal Tools
Nice to Haves
Safety
How to Solder
Best Practices
Prac App

## Slide 3: Overview
Different than welding
  More like brazing
Solder: conducts, low melting temperature
Iron: heats up, melts solder
Joins wires, PCBs, electronic components
Quickly: Soldering in the Dojo

## Slide 4: Soldering Irons
Gets hot
Like really hot
  Gets components hot!
  Will get you hot!
Parts
Tip types/sizes, changeability
Soldering Station
  Unregulated heat

## Slide 5: Solder
Alloy
  Pb, Tin
Conducts electricity
Spools, tubes
Different gauges
2 types: leaded and Lead Free

## Slide 6: Types of Solder
Leaded
Pb, Tin
Lower melting temperature
Sticks to itself
Does contain lead.
EU banned, CA Hard to find
Unleaded
Tin, copper, silver
No lead = higher melting temperature
  Station
More difficult to use
  “rosin core” / flux
Fumes

## Slide 7: Minimal Tools
Iron
Solder
Knife/wire strippers
Tape/heat shrink
Wire cutters/pliers

## Slide 8: Nice to Haves:
Helping hands
Flux
Sponge/brass sponge
Cradle
Station
Solder pump/vacuum/wick
Ventilator
PCB Vice
Adam Savage’s Rule of Tool Buying

## Slide 9
https://i.imgur.com/IGW8DcX.gifv

## Slide 10: Soldering Stations
Regulates heat of the iron
  w/o, get hotter and hotter
Varying levels
Cost vs niceness
Tailor to your level!
Plugs

## Slide 11: Safety
It gets hot
Fumes
  Ventilated room
  Ventilator
Leaded solder
NEVER SOLDER BATTERIES

## Slide 12: Soldering
Good solder joint
  “inside” wires
Strip wires
Join wires –
Apply flux
Apply iron
  1 second count
Apply solder
  Wait
Remove solder
Remove iron
Heat both ends to be soldered evenly
  Both wires
  Wire and the PCB
Heat your components, THEN add the solder
Side of the iron, NOT the tip
  “Sweet spot”

## Slide 15: Tinning the Iron’s Tip
Hot tips oxidize
Tinned tips are easier to use
Brass sponge/damp sponge
  “Buttering bread” motion
Place solder on tip, let it melt
Coat the tip in solder, let sit
Brush off extra solder

## Slide 16: Joining Wires
Laying on top
“Mash up”
Twist
Western Union Pigtail
  Best- NASA
“Wrong” is doesn’t conduct
  Bulky is inconvenient

## Slide 17: Western Union Pig Tail

## Slide 18: Practice!

## Slide 19: Soldering onto PCBs

## Slide 20: Best Practices/Pro Tips
“Sweet spot”
Pull the iron away quickly
Flush cut cutters

## Slide 21: Further Reading/Watching
https://learn.sparkfun.com/tutorials/how-to-solder---through-hole-soldering/soldering-irons

## Slide 22: Further Reading/Watching

## Slide 23: References

## Slide 24: References: Videos
https://www.youtube.com/watch?v=f95i88OSWB4
https://learn.adafruit.com/minty-boost/solder-it